## Slide 1: Accessory Dwelling Units Proposed Zoning Amendments
Planning Board Work Session/Public Hearing
January 30, 2023

## Slide 2: Purpose of these Revisions
Remove barriers and provide more flexibility
1
Strengthen provisions for neighborhood compatibility
2
Make the ordinance easier to understand and apply
3

## Slide 3: Outline of proposed changes
USE TABLE: Add more detail & fold Garden Cottages into Detached ADUs
PURPOSE & ELIGIBILITY: Expand opportunities for ADUs (use, density, size,
STANDARDS:
  All ADUs – Ownership, Owner-occupancy, # Bedrooms, Parking
  Attached ADUs – Size, Subordination Standards
  Detached ADUs – Size, Subordination Standards
ARCHITECTURAL DESIGN STANDARDS: Mass, Scale, Volume, Height & Architectural Style
REVIEW & APPROVAL PROCESS: As-of-Right and Conditional Use Permit
POST-APPROVAL REQUIREMENTS: Recorded Affidavit for Compliance

## Slide 4: Table of Uses – Attached ADUs (2)
Up to 750 sq. ft. and within an existing single-family dwelling.
More than 750 sq. ft. or expansion/addition to an existing dwelling.
P 7 districts
CUP 2 districts
CUP 9 districts

## Slide 5: Table of Uses – Detached ADUs (4)
Up to 600 sq. ft. and in an existing accessory building that complies with all dimensional standards for accessory buildings.
Up to 600 sq. ft. in an existing accessory building where existing building does not comply with all standards, requires a modification of standards, a variance, or includes an expansion.
Up to 1,000 sq. ft. in a new building that does not comply with all dimensional standards or requires any variance.
Up to 750 sq. ft. in a new building that complies with all lot and building standards for a single-family dwelling.
P
7 districts
CUP
3 districts
CUP
7 districts
CUP
7 districts

## Slide 6: Purpose and Eligibility
Revised statement of purpose to include affordability and expansion of the housing stock within existing developed areas to meet local housing needs while minimizing adverse impacts to surrounding neighborhood.
Clarify that ADUs are subject to all applicable municipal standards for single-family dwellings (zoning and non-zoning), except:
  Minimum lot area per dwelling unit; and
  Existing accessory buildings – shall comply with the dimensional standards for accessory structures.

## Slide 7: Revised Standards – All ADUs – Parking
2 spaces for principal single-family dwelling, PLUS
1 space for ADU up to 750 sq. ft.
2 spaces for ADU more than 750 sq. ft.

## Slide 8: Revised Standards – Attached ADUs
Increase in floor area up to 1,000 sq. ft. by conditional use permit.
Subordination to the existing single family dwelling:
Addition or expansion must be recessed or projected at least 18 inches from the existing front wall;
Addition that includes a garage facing the street must be set back at least 10 feet from the existing front wall;
A Single-story dwelling may be expanded vertically by one story or horizontally at the same height as the existing dwelling; and
Addition or expansion of a non-single-story dwelling that includes horizontal expansion must be no higher than 75% of the height of the existing structure.

## Slide 9: Revised Standards – Detached ADUs – SIZE
MAXIMUM SIZE OF DETACHED ADU:
  750 sq. ft.
  Where permitted in the use table: 1,000 sq. ft. by CUP
MAXIMUM EXPANSION OF EXISTING ACCESSORY BUILDING:
  750 sq. ft.
MAXIMUM SIZE OF BUILDING CONTAINING THE DETACHED ADU
  1,600 sq. ft. or 75% of principal building’s floor area.

## Slide 10: Revised Standards – Detached ADUs – SUBORDINATION
New building shall be placed at least 10 feet further from front lot line than existing building
Building height no greater than 22 feet;
Increased setbacks from all property lines if DADU is taller than principal dwelling;
Building footprint no greater than 750 sq. ft.;
Building with and DADU no greater than 1,600 SF
Dormers only outside required setbacks and no more than 1/3 of roof plane area;
Compliance with drainage and lighting requirements of the zoning ordinance; and
Compliance with minimum building separation requirements of the building code.

## Slide 11: ARCHITECTURAL DESIGN STANDARDS – CONSISTENCY
Massing
Architectural style
Roof forms
Siding material
Windows
Doors
Trim
Foundation
Projections, including dormers, porticos, bays, porches, door canopies
Chimneys, balconies, railings, gutters, shutters

## Slide 12: POST-APPROVAL REQUIREMENTS
Recordable Affidavits by Applicants.
Annual Staff Review for a Certificate of Compliance:
  Ownership & Occupancy

## Slide 13: OTHER PROVISIONS
ARTICLE 11 – OFF-STREET PARKING
  Location of parking spaces: conform ADU to single-family (per State statute).
ARTICLE 15 – DEFINITIONS
  Revise “Accessory building or structure”
  Revise “Detached accessory dwelling unit”
  Delete “Garden cottage”

## Slide 14: Accessory Dwelling Units Proposed Zoning Amendments
Planning Board Work Session/Public Hearing
January 30, 2023
NEXT STEPS:
Adoption of the ADU Amendments
Supplemental ADU Handbook including:
Submission Requirements
Sample Application
Flow Chart of Steps
Example Site Plans, Floor Plans & Elevations
Annual Tracking:
Housing Production
Location & Type
Post Mortems on Design & Fit

## Slide 15: Accessory Dwelling Units Proposed Zoning Amendments
Planning Board Work Session/Public Hearing
January 30, 2023
QUESTIONS AND COMMENTS